## Slide 1
Convolutional Layer
Expensive Multipliers
Store and Load Lots of Parameters
H
R
S
C
input fmap
output fmap
C
filter
E
W
F
Batch Normalization
Activation
Replaced with Fixed Function Blocks!
Notes: So, let look more closely to a convolutional layer computations. We have filters (weights) that need to multiplied with input feature map and then apply some functions like bn and activation functions to generate one pixel of output. As you can see, we need expensive multipliers. We also need to store and load lots of parameters. What can we do? Here is the main Idea of Nulla project, replace weights and multiplication with fixed function blocks.

## Slide 2
Fixed Function-based Computations
fixed function logic
H
input fmap
output fmap
C
E
W
F
E
output fmap
Many
Output Channels (M)
M
H
input fmap
C
W
F
fixed function logic
Accuracy degradation
Notes: Produces filter outputs by replacing filters with fixed function
logic/arithmetic blocks
Eliminates many of costly MAC operations and corresponding
weight memory accesses
Improves latency and energy efficiency by orders of magnitude with a tolerable loss in the inference accuracy
Define a high-level function, flatten the design, and apply EDA algorithms.
Implement the shared logic once and provide its outputs to neurons that consume it.
The optimized logic requires 7 logic gates while implementing each neuron individually requires 13 logic gates in total.
Reduce adders and multiplexers to a group of logic gates.
Similarly, one can optimize consecutive layers across the neural network.
The main bottleneck here is the accuracy degradation. How can we compensate it?